## Slide 1
AES
Add-on processor for RISC-V
Students: David Dan
Dolev Vaknin
Supervisor: Eric Herbelin

## Slide 2
In our days, where we use sensors and processors anywhere and anytime, it’s getting
very hard to keep our data safe.
There are a lot of chances to steal the information between collecting the raw data by a sensor, and encryption of that data by our processor.
The goal of this project is to design and implement an AES encryption (or any other safe encryption method) inside RISC-V processor, which can be positioned adjacent to a sensor.
In this project we are using RI5CY core embedded in Pulpenix microcontroller.
abstract
Introduction
AES algorithm
Workflow
Performance
Simulation

## Slide 3: background
RISC-V
  Open ISA
  Founded by University of Berkeley, California.
  Adopted by many in both academy and industry.
PULP
  Parallel Ultra Low Power open-source computing platform
  A collaboration of ETH Zurich and University of Bologna.
PULPino
  Based on PULP platform.
  Uses RI5CY core.
PULPeniX
  Developed in Bar Ilan, Enics lab.
  A HW and SW development and simulation environment.
AES
  Advanced Encryption Standard - specification for the encryption of electronic data.
  Based on a design principle known as a substitution–permutation network.
3

## Slide 4
Goals
Knowing RISC-V PULPINO infrastructure
  Based on Michael and Avi project.
Integrating AES in RISC-V environment
  AES accelerator and designated new commands (While maintaining backward compatibility).
Demonstrate advantages in terms of performance
  We expect to increase in power, area (decrease in performance).
4

## Slide 5
Possible solutions – pros and cons
 | Encryption from buffer | Encryption on-the-fly | Encryption command
Pros | Relatively secure Relatively Easy to implement | Easy to implement Encryption in early stages Economical | Can store one encrypted register
Cons | Need to encrypt 4 registers (128-bit) Requires a lot more area. | Not secure (not AES) | Not very secure Hard to implement Slow down the processor
5

## Slide 6
AES algorithm
Key
Plain-Text
Key Expansion Unit
Round Key (0)
SubBytes
ShiftRows
MixColumn
Round Key (9)
SubBytes
ShiftRows
Round Key (10)
Cipher text
AES encryption is done in several rounds (10 rounds for 128 bit key), and each one of the rounds is consist of several processing steps.
…
…
6
background
AES algorithm
Workflow
Performance
Simulation

## Slide 7
KeyExpansion
  Expanding the given key with 128 bits to 1408 bits using Rijndael's key schedule.
RotWord
SubWord
Rcon
7

## Slide 8
  SubBytes
    A non-linear substitution step where each byte is replaced with another according to a lookup table.
SubBytes
8

## Slide 9
ShiftRows
A transposition step where the last three rows of the state are shifted cyclically a certain number of steps.
9

## Slide 10
  MixColumns (except for the last round)
    A linear mixing operation which operates on the columns of the state, combining the four bytes in each column.
MixColumns
10

## Slide 11
  AddRoundKey
  Each byte of the state is combined with a byte of the round key using bitwise xor. (twice in the first round - in the beginning and in the end of the round)
11

## Slide 12
RI5CY Core
12

## Slide 13
Architecture
  Flow
  Modules
Implementation
  Per module implementation
  Specific module simulation.
Integration
  Decode stage.
  Write-Back stage.
Simulation
  Full AES simulation.
  Comparison to C implementation.
Extensions
  Accessories
  Automations
Workflow
13
background
AES algorithm
Workflow
Performance
Simulation

## Slide 14
Base architecture - selected solution
AES engine
AES register file
AES WB
128-bit data
128-bit key
32-bit
128-bit data
128-bit ciphered
32-bit
14

## Slide 15
Commands structure
Opcode
AES register (key or data)
AES function
RISCV register
Not in use
0x3b
0x[0-3]
0x[0-3]
0x[0-31]
0x0
0x0
15

## Slide 16
AES Engine Architecture
16

## Slide 17
AES Register File Architecture
17

## Slide 18
AES Write Back Architecture
18

## Slide 19
AES Write Back FSM
19

## Slide 20
Performance
 | GenPro PULPenix | GenPro PULPenix AES
Timing (slack) |  | 
Area |  | 
Power |  | 
CoreMark |  | 
 | GenPro PULPenix | GenPro PULPenix AES
Timing (slack) |  | 
Area |  | 
Power |  | 
CoreMark |  | 
20
background
AES algorithm
Workflow
Performance
Simulation

## Slide 21
Simulation
21
background
AES algorithm
Workflow
Performance
Simulation

## Slide 22
Register file simulation
22

## Slide 23
AES engine simulation
23

## Slide 24
AES WB simulation
24

## Slide 25
AES verification test
25

## Slide 26
Conclusions
Successfully integrate AES engine inside RISCV core
  Minimal effect on power and timing performance
  Significant effect on area
Create user friendly AES commands support
  Add compiling scripts that run before GNU’s compiler
  Create AES verification script
Improve existing simulation scripts
  Improve GenPro setup script
  Add new simulation options
Add synthesis script
  No need to open dc_shell to synthesize the project
26