## Slide 1
AES
Add-on processor for RISC-V
Students: David Dan
Dolev Vaknin
Supervisor: Eric Herbelin
Semester: Winter 2019

## Slide 2
In our days, where we use sensors and processors anywhere and anytime, it’s getting
very hard to keep our data safe.
There are a lot of chances to steal the information between collecting the raw data by a sensor, and encryption of that data by our processor.
The goal of this project is to design and implement an AES encryption (or any other safe encryption method) inside RISC-V processor.
In this project we are using RI5CY core embedded in Pulpenix microcontroller.
abstract

## Slide 3: background
RISC-V is an open ISA
    Founded by University of Berkeley, California.
    Adopted by many in both academy and industry.
PULP
    Parallel Ultra Low Power open-source computing platform
    A collaboration of ETH Zurich and University of Bologna.
PULPino processor
    Based on PULP platform.
    Uses RI5CY core.
PULPeniX
    Developed in Bar Ilan, Enics lab.
    A HW and SW development and simulation environment.
AES
  Advanced Encryption Standard - specification for the encryption of electronic data, based on a design principle known as a substitution–permutation network.

## Slide 4
Goals
Knowing RISC-V PULPINO infrastructure
  Based on Michael and Avi project.
Integrating AES in RISC-V environment
  AES accelerator and designated new commands (While maintaining backward compatibility).
Demonstrate advantages in terms of performance
  We expect to increase in power and decrease in performance.

## Slide 5
Possible solutions – pros and cons
 | Encryption from buffer | Encryption on-the-fly | Encryption command
Pros | Relatively secure Relatively Easy to implement | Easy to implement Encryption in early stages | Can store one encrypted register
Cons | Need to encrypt 4 registers (128-bit) Slow down the processor | Not very secure (not AES) | Not the most secure method Hard to implement Slow down the processor

## Slide 6
AES algorithm
Key
Plain-Text
Key Expansion Unit
Round Key (0)
SubBytes
ShiftRows
MixColumn
Round Key (9)
SubBytes
ShiftRows
Round Key (10)
Cipher text
AES encryption is done in several rounds (10 rounds for 128 bit key), and each one of the rounds is consist of several processing steps.
…
…

## Slide 7
KeyExpansion
  Expanding the given key with 128 bits to 1408 bits using Rijndael's key schedule.
RotWord
SubWord
Rcon

## Slide 8
  SubBytes
    A non-linear substitution step where each byte is replaced with another according to a lookup table.
SubBytes

## Slide 9
ShiftRows
A transposition step where the last three rows of the state are shifted cyclically a certain number of steps.

## Slide 10
  MixColumns (except for the last round)
    A linear mixing operation which operates on the columns of the state, combining the four bytes in each column.
MixColumns

## Slide 11
  AddRoundKey
  Each byte of the state is combined with a byte of the round key using bitwise xor. (twice in the first round - in the beginning and in the end of the round)

## Slide 12
Base architecture of the selected solution
AES engine
AES register file
AES WB
128-bit data
128-bit key
32-bit
128-bit data
128-bit ciphered
32-bit

## Slide 13
Commands structure
0x3b
0x[0-3]
0x[0-3]
0x[0-31]
0x0
0x0

## Slide 14
AES Engine Architecture

## Slide 15
AES Register File Architecture

## Slide 16
AES Write Back Architecture